## Slide 1: RGB-D Images and Applications
Yao Lu

## Slide 2: Outline
Overview of RGB-D images and sensors
Recognition: human pose, hand gesture
Reconstruction: Kinect fusion

## Slide 3: Outline
Overview of RGB-D images and sensors
Recognition: human pose, hand gesture
Reconstruction: Kinect fusion

## Slide 5
How does Kinect work?
Kinect has 3 components :-
color camera ( takes RGB values)
IR camera ( takes depth data )
Microphone array ( for speech recognition )

## Slide 6: Depth Image

## Slide 7: How Does the Kinect Compare?
Distance Sensing
  Alternatives Cheaper than Kinect
  ~$2 Single-Point Close-Range Proximity Sensor
Motion Sensing and 3D Mapping
  High Performing Devices with Higher Cost
Good Performance for Distance and Motion Sensing
Provides a bridge between low cost and high performance sensors

## Slide 8: Depth Sensor
IR projector emits predefined Dotted Pattern
Lateral shift between projector and sensor
  Shift in pattern dots
Shift in dots determines Depth of Region

## Slide 9: Kinect Accuracy
OpenKinect SDK
11 Bit Accuracy
  211 = 2048 possible values
Measured Depth
  Calculated 11 bit value
  2047 = maximum distance
    Approx. 16.5 ft.
  0 = minimum distance
    Approx. 1.65 ft.
Reasonable Range
  4 – 10 feet
  Provides Moderate Slope
Values from: http://mathnathan.com/2011/02/depthvsdistance/

## Slide 10: Kinect Accuracy
OpenKinect SDK
11 Bit Accuracy
  211 = 2048 possible values
Measured Depth
  Calculated 11 bit value
  2047 = maximum distance
    Approx. 16.5 ft.
  0 = minimum distance
    Approx. 1.65 ft.
Reasonable Range
  4 – 10 feet
  Provides Moderate Slope
Values from: http://mathnathan.com/2011/02/depthvsdistance/

## Slide 11: Other RGB-D sensors
Intel RealSense Series
Asus Xtion Pro
Microsoft Kinect V2
Structure Sensor

## Slide 12: Outline
Overview of RGB-D images and sensors
Recognition: human pose, hand gesture
Reconstruction: Kinect fusion

## Slide 13: Recognition: Human Pose recognition
Research in pose recognition has been on going for 20+ years.
Many assumptions: multiple cameras, manual initialization, controlled/simple backgrounds

## Slide 14
Model-Based Estimation of 3D Human Motion, Ioannis Kakadiaris and Dimitris Metaxas, PAMI 2000

## Slide 15
Tracking People by Learning Their Appearance, Deva Ramanan, David A. Forsyth, and Andrew Zisserman, PAMI 2007

## Slide 16: Kinect
Why does depth help?

## Slide 17: Algorithm design
Shotton et al. proposed two main steps:
1. Find body parts
2. Compute joint positions.
Real-Time Human Pose Recognition in Parts from Single Depth Images
Jamie Shotton Andrew Fitzgibbon Mat Cook Toby Sharp Mark Finocchio
Richard Moore Alex Kipman Andrew Blake, CVPR 2011

## Slide 18: Finding body parts
What should we use for a feature?
What should we use for a classifier?

## Slide 19: Finding body parts
What should we use for a feature?
  Difference in depth
What should we use for a classifier?
  Random Decision Forests
    A set of decision trees

## Slide 20: Features
: depth at pixel x in image I
: parameters describing offsets

## Slide 21: Classification
Learning:
Randomly choose a set of thresholds and features for splits.
Pick the threshold and feature that provide the largest information gain.
Recurse until a certain accuracy is reached or depth is obtained.

## Slide 22: Implementation details
3 trees (depth 20)
300k unique training images per tree.
2000 candidate features, and 50 thresholds
One day on 1000 core cluster.

## Slide 23: Synthetic data

## Slide 24: Synthetic training/testing

## Slide 25: Real test

## Slide 26: Results

## Slide 27: Estimating joints
Apply mean-shift clustering to the labeled pixels.
“Push back” each mode to lie at the center of the part.

## Slide 28: Results

## Slide 29: Outline
Overview of RGB-D images and sensors
Recognition: human pose, hand gesture
Reconstruction: Kinect fusion

## Slide 30: Hand gesture recognition

## Slide 31
Target: low-cost markerless mocap
  Full articulated pose with high DoF
  Real-time with low latency
Challenges
  Many DoF contribute to model deformation
  Constrained unknown parameter space
  Self-similar parts
  Self occlusion
  Device noise
Hand Pose Inference

## Slide 32
Pipeline Overview
Tompson et al. Real-time continuous pose recovery of human hands using convolutional networks. ACM SIGGRAPH 2014.
Supervised learning based approach
  Needs labeled dataset + machine learning
  Existing datasets had limited pose information for hands
Architecture
OFFLINE DATABASE CREATION
CONVNET JOINT DETECT
RDF
HAND DETECT
INVERSE KINEMETICS
POSE

## Slide 33
Pipeline Overview
Supervised learning based approach
  Needs labeled dataset + machine learning
  Existing datasets had limited pose information for hands
Architecture
OFFLINE DATABASE CREATION
CONVNET JOINT DETECT
RDF
HAND DETECT
INVERSE KINEMETICS
POSE

## Slide 34
Pipeline Overview
Supervised learning based approach
  Needs labeled dataset + machine learning
  Existing datasets had limited pose information for hands
Architecture
OFFLINE DATABASE CREATION
CONVNET JOINT DETECT
RDF
HAND DETECT
INVERSE KINEMETICS
POSE

## Slide 35
Pipeline Overview
Supervised learning based approach
  Needs labeled dataset + machine learning
  Existing datasets had limited pose information for hands
Architecture
OFFLINE DATABASE CREATION
RDF
HAND DETECT
CONVNET JOINT DETECT
INVERSE KINEMETICS
POSE

## Slide 36
RDF Hand Detection
Per-pixel binary classification  Hand centroid location
Randomized decision forest (RDF)
  Shotton et al.[1]
  Fast (parallel)
  Generalize
[1] J. Shotten et al., Real-time human pose recognition in parts from single depth images, CVPR 11
Target
Inferred
RDT1
RDT2
+
P(L | D)
Labels

## Slide 37: Inferring Joint Positions
PrimeSense
Depth
ConvNet
Depth
ConvNet Detector 1
ConvNet Detector 2
ConvNet Detector 3
Image Preprocessing
2 stage Neural Network
HeatMap
96x96
48x48
24x24

## Slide 38: Hand Pose Inference
Results

## Slide 39: Outline
Overview of RGB-D images and sensors
Recognition: human pose, hand gesture
Reconstruction: Kinect fusion

## Slide 40: Reconstruction: Kinect Fusion
Newcombe et al. KinectFusion: Real-time dense surface mapping and tracking. 2011 IEEE International Symposium on Mixed and Augmented Reality.
https://www.youtube.com/watch?v=quGhaggn3cQ

## Slide 41: Motivation
Augmented Reality
3d model scanning
Robot Navigation
Etc..

## Slide 42: Challenges
Tracking Camera Precisely
Fusing and De-noising Measurements
Avoiding Drift
Real-Time
Low-Cost Hardware

## Slide 43: Proposed Solution
Fast Optimization for Tracking, Due to High Frame Rate.
Global Framework for fusing data
Interleaving Tracking & Mapping
Using Kinect to get Depth data (low cost)
Using GPGPU to get Real-Time Performance (low cost)

## Slide 44: Method

## Slide 45: Tracking
Finding Camera position is the same as fitting frame’s Depth Map onto Model
Tracking
Mapping

## Slide 46: Tracking – ICP algorithm
icp = iterative closest point
Goal: fit two 3d point sets
Problem: What are the correspondences?
Kinect fusion chosen solution:
  Start with
  Project model onto camera
  Correspondences are points with same coordinates
  Find new T with Least - Squares
  Apply T, and repeat 2-5 until convergence
Tracking
Mapping

## Slide 47: Tracking – ICP algorithm
icp = iterative closest point
Goal: fit two 3d point sets
Problem: What are the correspondences?
Kinect fusion chosen solution:
  Start with
  Project model onto camera
  Correspondences are points with same coordinates
  Find new T with Least - Squares
  Apply T, and repeat 2-5 until convergence
Tracking
Mapping

## Slide 48: Tracking – ICP algorithm
Assumption: frame and model are roughly aligned.
True because of high frame rate
Tracking
Mapping

## Slide 49: Mapping
Mapping is Fusing depth maps when camera poses are known
  Model from existing frames
  New frame
Problems:
  measurements are noisy
  Depth maps have holes in them
Solution:
  using implicit surface representation
  Fusing = estimating from all frames relevant
Tracking
Mapping

## Slide 50: Mapping – surface representation
Surface is represented implicitly - using Truncated Signed Distance Function (TSDF)
Numbers in cells measure voxel distance to surface – D
Voxel grid
Tracking
Mapping

## Slide 51: Mapping
Tracking
Mapping

## Slide 52: Mapping
d= [pixel depth] – [distance from sensor to voxel]
Tracking
Mapping

## Slide 53: Mapping
Tracking
Mapping

## Slide 54: Mapping
Tracking
Mapping

## Slide 55: Mapping
Tracking
Mapping

## Slide 56: Method

## Slide 57: Pros & Cons
Pros:
  Really nice results!
    Real time performance (30 HZ)
    Dense model
    No drift with local optimization
    Robust to scene changes
  Elegant solution
Cons :
  3d grid can’t be trivially up-scaled

## Slide 58: Limitations
doesn’t work for large areas (Voxel-Grid)
Doesn’t work far away from objects (active ranging)
Doesn’t work out-doors (IR)
Requires powerful Graphics card
Uses lots of battery (active ranging)
Only one sensor at a time